## Slide 1
FINAL DESIGN PROJECT
iCAN
Assistive navigation system for safer independent mobility
ECE 441 Spring 2026 · Smart and Connected Embedded System Design
Instructor: Prof. Jafar Saniie
Ariel Nyamien
Aiden Verdin
Alex Stokrp
Saber Garibi
CANE + EYE + APP
iCAN · Group 5 · ECE 441 Spring 2026
1
Notes: Open with the project identity: iCAN is a connected assistive navigation ecosystem, not just a smart cane. Mention final deliverable context and team.

## Slide 2
Executive snapshot
What we built and why it matters
Problem
Traditional white canes detect ground-level obstacles well but miss head-height hazards, provide limited distance context, and do not integrate navigation or scene awareness.
Solution
iCAN combines directional obstacle sensing, haptic feedback, BLE telemetry, mobile accessibility UX, and an optional camera-based scene description layer.
Impact
The system extends perception ahead of the user, preserves hands-free interaction, and moves compute-heavy AI to the phone for better latency, battery use, and upgradability.
Cane
LiDAR + ultrasonic + IMU + haptics
Eye
ESP32-S3 camera + BLE image stream
App
Flutter + BLE + TTS + AI vision
User
Spatial audio + haptics
Design principle: keep immediate safety feedback local, use the phone for richer context.
Notes: Frame the system in one sentence: iCAN pairs immediate local safety feedback with phone-based intelligence.

## Slide 3
Navigation gaps we are targeting
The device focuses on hazards that are hard to perceive with a standard cane.
40%
blind individuals report head-height collisions
43%
visually impaired users successfully complete street crossings
2m+
target detection range ahead of the user
Why this is embedded systems work
The problem requires sensing, timing, power management, BLE communication, actuator feedback, and user-safe failure behavior — not just an app.
Head-height hazards
branches · signs · shelves · awnings
Distance ambiguity
near vs. far obstacles need different urgency
Situational awareness
text · people · scene layout · landmarks
Navigation load
turns must not mask obstacle alerts
iCAN · Group 5 · ECE 441 Spring 2026
2
Notes: Use this slide to connect the human problem to the engineering requirements: sensing range, feedback encoding, and safety prioritization.

## Slide 4
System overview
Two embedded devices and one accessibility-first mobile client.
iCAN Cane
Arduino Nano ESP32
LiDAR + ultrasonic
IMU + haptics + GPS
iCAN Eye
XIAO ESP32-S3 Sense
OV2640 camera
JPEG image stream
Mobile App
Flutter client
BLE control plane
TTS + scene description
Local AI
Apple Vision
CoreML depth/object
On-device fallback
Cloud AI
Gemini vision
When online/user-selected
BLE
BLE image chunks
Notes: Describe the split: cane handles real-time safety; eye captures scene imagery; app orchestrates BLE, speech, and AI backend selection.

## Slide 5
User interaction flow
Immediate haptics first; speech when richer context is needed.
1
Walk normally
Cane continuously samples obstacle sensors and IMU.
2
Detect hazard
Firmware maps obstacle side and distance into haptic urgency.
3
Optional capture
User triggers iCAN Eye for a scene description.
4
Phone interprets
App receives image data and chooses local/cloud AI path.
5
Act safely
User receives directional vibration and spoken spatial context.
Safety priority rule: local obstacle alerts must override slower navigation or AI descriptions.
Notes: Walk through a realistic use case. Stress that the system is not trying to replace the cane; it extends feedback.

## Slide 6
Hardware architecture
Sensors and actuators map directly to user-facing feedback.
Cane controller
Arduino Nano ESP32 coordinates sensing, BLE telemetry, event detection, and haptic output.
Obstacle sensing
TF-Luna/ToF and ultrasonic sensing provide near/far and head/waist-level obstacle coverage.
Motion + health
LSM6DSOX IMU supports fall detection/orientation; pulse and battery telemetry support monitoring.
Feedback
DRV2605L and vibration motors encode direction and urgency through touch.
LiDAR/ToF
head-height + spatial grid
Ultrasonic
lower obstacle zones
IMU
yaw + fall events
GPS
location + guided nav
BLE
app telemetry
Haptics
left/right/top motors
BOM highlights: Arduino Nano ESP32, XIAO ESP32-S3 Sense, TF-Luna/ToF, ultrasonic sensors, LSM6DSOX, DRV2605L, vibration motors, GPS, Li-Po batteries.
Notes: Covers the report requirement for hardware, sensors, actuators, and system constraints.

## Slide 7
Obstacle detection → haptic language
The user should feel direction, distance, and urgency without looking at a screen.
Left/right ultrasonics
waist-level obstacles
side-specific alerts
Top LiDAR/ToF
head-height hazards
branches/signs/awnings
IMU sweep filter
reduces false positives
from natural cane motion
Haptic driver
distance-scaled
pulse/intensity patterns
2–4 m: intermittent pulse
1–2 m: continuous vibration
<1 m: strong vibration
Feedback rule: the closest safety event wins over navigation guidance.
iCAN · Group 5 · ECE 441 Spring 2026
3
Notes: Explain the tactile language. Distance and side are turned into vibration patterns, not text.

## Slide 8
Cane firmware structure
Modular firmware keeps sensing, events, power, and feedback testable.
Sensor layer
LiDAR · ultrasonic · IMU · pulse · GPS · battery
Event detection
obstacle side · fall flag · low battery · sensor health
State manager
normal · low power · emergency · sleep
Response layer
haptic · LED · buzzer · BLE notify
App telemetry
battery % · BPM · yaw · GPS · status
Power management
Firmware documentation reports sleep modes that reduce idle draw from always-active behavior into staged low-power states.
Safety behavior
Fall alert logic avoids indefinite buzzer activation and caps emergency behavior to prevent battery drain.
Protocol discipline
A shared BLE protocol file mirrors packet fields in C++ firmware and Dart app code to avoid mismatch bugs.
Evidence source: firmware/protosmart_cane STATUS_REPORT, DEPLOYMENT_CHECKLIST, and protocol/ble_protocol.yaml.
Notes: This slide maps directly to software/hardware integration and original code contributions.

## Slide 9
iCAN Eye: scene awareness pipeline
Camera hardware captures the world; the phone turns it into speech.
ESP32-S3 Eye
OV2640 capture
button trigger
BLE stream
JPEG chunks
sequence numbers
Phone vision
Apple Vision
Depth + objects + OCR
Speech
4–6 sentence
spatial description
Layer 1 perception
OCR, scene classification, human detection, depth estimation, and object boxes run as structured perception.
Layer 2 understanding
A VLM backend adds holistic image interpretation when local model or cloud mode is available.
Layer 3 speech synthesis
The app converts perception into short, practical, clock-position guidance.
Notes: This is the “wow” software slide: phone-side AI makes the embedded camera useful without forcing the ESP32 to run heavy models.

## Slide 10
Mobile app architecture
Flutter app as the accessible command center.
Accessibility-first UI
WCAG AAA-oriented theme, Semantics wrappers, large controls, VoiceOver/TalkBack design.
BLE services
Dual-device connection management, image reassembly, telemetry streams, saved device IDs.
Speech loop
TTS output, voice-command direction, and scene-description history for repeatable feedback.
HomeViewModel
state orchestration
BleService
scan/connect/packets
SceneService
backend selection
VisionChannel
Swift/CoreML bridge
TTS
audio output
Tech stack: Dart/Flutter, Provider MVVM, GoRouter, flutter_blue_plus, CoreML/Vision Swift channels, Gemini fallback.
iCAN · Group 5 · ECE 441 Spring 2026
4
Notes: Ground this in the actual repo QA technical briefing.

## Slide 11
BLE protocol and data model
A shared protocol keeps firmware and app behavior aligned.
Cane service
Navigation commands, obstacle alerts, IMU telemetry, cane status, GPS data.
Eye service
Instant text, JPEG image stream, capture/profile/status commands.
Packet discipline
Little-endian telemetry, explicit fields, and documented image sequence headers.
App → Cane
NAV_LEFT
NAV_RIGHT
STOP
Cane → App
obstacle
fall flag
battery
App → Eye
CAPTURE
LIVE_START
PROFILE
Eye → App
text
image chunks
App → User
speech
alerts
haptics
Single source of truth: protocol/ble_protocol.yaml mirrors firmware/shared/ble_protocol.h and lib/protocol/ble_protocol.dart.
Notes: Use this as the systems engineering proof: packet names, directions, and payload fields exist in the repo.

## Slide 12
Power, packaging, and constraints
The design is constrained by weight, runtime, weather, and user comfort.
Runtime target
Prior deck target: 8–10 hour operating goal; firmware emphasizes staged power modes and battery telemetry.
Physical layout
Handle houses haptic motors; sensors mount below/top of handle with wiring strain relief and shock mounting.
Weather & durability
Prior design target includes IP65-style considerations: gaskets, venting, connectors, and robust mounting.
Safety
Failsafe behavior: obstacle alerts remain local; cloud AI is optional, not required for basic safety.
Active
100% duty
Use case
mixed sensing
Low power
reduced draw
Emergency
bounded alert
Notes: Talk about engineering tradeoffs: runtime, weight, durability, and local fallback behavior.

## Slide 13
Security and responsible design
Assistive technology must be useful without becoming invasive.
Privacy
Image processing is designed to run locally when possible; cloud vision is a selected/fallback path, not the only path.
Safety
The cane’s local obstacle feedback does not depend on internet access, cloud services, or a perfect AI caption.
Transparency
The app should speak concise spatial context and avoid overclaiming uncertain detections.
Security
BLE command scope is narrow: navigation commands, telemetry, capture/status, and documented packet formats.
Ethical design stance
Prioritize user autonomy, preserve safety-critical functions offline, and make AI assistance explainable enough to trust but bounded enough not to mislead.
iCAN · Group 5 · ECE 441 Spring 2026
5
Notes: This slide supports both final presentation expectations and later ethics/report work.

## Slide 14
Related work and differentiation
iCAN is positioned between simple smart canes and phone-only navigation aids.
System
Strength
Gap
iCAN response
Traditional white cane
Reliable, low-cost, passive
Limited range; poor head-height detection
iCAN extends sensing while preserving cane use
WeWalk / smart canes
Commercial precedent for connected cane systems
High cost; limited customization
Course prototype explores open, modular architecture
Phone-only vision apps
Powerful AI descriptions
No immediate tactile obstacle feedback
iCAN separates local safety from rich scene context
Wearable navigation systems
Hands-free perception
Can be bulky or opaque
iCAN uses cane + necklace + phone split
Notes: Keep this concise. It satisfies related work/comparison without spending too much presentation time.

## Slide 15
Implementation progress and validation evidence
The project has working software structure and documented firmware verification paths.
Mobile app
Flutter app includes BLE service, accessible screens, scene-description service, TTS, device pairing, settings, and diagnostic screens.
iCAN Eye
Firmware was refactored into camera, BLE, and main orchestration modules with build environments for main, camera, and BLE stream testing.
Cane firmware
ProtoSmartCane v2.0 documentation covers battery monitoring, sleep modes, haptic driver, fall alert handling, and deployment checks.
Repo
Codebase and docs are centralized in GitHub for review.
Verification currently documented
PlatformIO build environments for iCAN Eye modules
Shared BLE protocol mirrored across firmware/app
App architecture briefing with dependencies and file structure
Deployment checklist for hardware field tests
Project repo: https://github.com/saberrg/ican
Notes: Be careful not to overclaim live field-test results. Present this as implementation and validation evidence.

## Slide 16
Recorded demo plan
Use the 5+ minute demo block to prove the system, not just describe it.
1
Cane sensing
Show obstacle approach and haptic direction/intensity response.
2
BLE telemetry
Show app connection/status and battery/IMU/alert fields.
3
Eye capture
Trigger capture and show image/description flow.
4
Accessibility UX
Demonstrate spoken output, large controls, and blind-user-oriented flow.
Suggested timing: ~8–9 minutes slides + ~5–6 minutes demo = under 15 minutes total.
iCAN · Group 5 · ECE 441 Spring 2026
6
Notes: This is tactical: it tells the team exactly what to record for the required video.

## Slide 17
Remaining work and future improvements
The final system has a clear path from prototype to deployable assistive device.
Hardware field trial
Validate sensor placement, vibration interpretation, battery estimates, and comfort in walking tests.
Guided navigation
Integrate Mapbox/walking directions and tune haptic turn timing around obstacle override rules.
Vision optimization
Benchmark local VLM quality/latency and improve spatial descriptions with depth + object fusion.
Safety review
Improve privacy controls, BLE pairing rules, and failure-mode documentation.
Prototype → verified demo → user-centered field testing → refinement → deployable design
Prototype
Demo
Field test
Refine
Deploy
Notes: Future work should sound credible and prioritized, not like feature creep.

## Slide 18
Team member work contributions
Final report and presentation must clearly describe each member’s tasks.
Ariel Nyamien
Power and hardware design: sensor/actuator selection, packaging constraints, electrical integration support.
Aiden Verdin
Controls and embedded systems: firmware logic, sensor processing, state behavior, hardware testing support.
Alex Stokrp
Hardware and circuit design: schematic/BOM support, packaging, sensor placement, physical integration.
Saber Garibi
Software/app architecture: Flutter app, BLE protocol integration, AI vision pipeline, repo documentation.
Note: confirm/edit contribution wording before final submission so it matches the team’s actual work split.
Notes: This slide is intentionally editable. Saber/team should confirm exact contribution wording before submission.

## Slide 19
Conclusion
iCAN extends mobility feedback without taking control away from the user.
A practical assistive navigation system should be immediate, understandable, and resilient.
Immediate
Obstacle feedback is local and tactile, so basic safety does not depend on cloud AI.
Understandable
Haptics encode side/distance; speech describes spatial context in plain language.
Resilient
The cane, eye, and app are modular, documented, and independently testable.
iCAN is a connected ecosystem: embedded sensing for safety, mobile compute for intelligence, and accessible feedback for the user.
iCAN · Group 5 · ECE 441 Spring 2026
7
Notes: End with the core claim: local safety + mobile intelligence + accessibility-first feedback.

## Slide 20
References and source material
Key sources used for the final deck.
Bourne et al., “Global prevalence of blindness and vision impairment,” The Lancet Global Health, 2017. https://doi.org/10.1016/S2214-109X(17)30293-0
iCAN GitHub repository and project documentation: https://github.com/saberrg/ican
Nano ESP32 / XIAO ESP32-S3 / sensor datasheets listed in prior project references and BOM.
Apple Core ML and Vision documentation for on-device perception pipeline.
Moondream project reference for VLM experimentation: https://github.com/vikhyat/moondream
ECE 441 final project requirements and evaluation material from Canvas.
Notes: References slide can be expanded if required by the team report/paper, but keep it concise for the presentation.